PRODUCT NAME:     Desktop socket

PRODUCT No.:     FZ-510

包含要素：

1、基础参数

2、产品规格

3、产品应用

4、产品展示

5、产品卖点

6、产品勾线图

7、产品安装步骤

8、安装注意事项

9、包装方案

Characteristic:

| 1 | Model | FZ-510 | 7 | Market standard | Customized |
| --- | --- | --- | --- | --- | --- |
| 2 | Brand Name | Safewire or OEM brand | 8 | Place of origin | Zhejiang , Wenzhou, China |
| 3 | Type | Desk pop up socket | 9 | Frequency | 50Hz~60Hz |
| 4 | Color | Black/Silver | 10 | Current Type | AC |
| 5 | Grounding | Standard grounding | 11 | Rated Current | 10-25A |
| 6 | HS Code | 8536690000 | 12 | Voltage | 95~260V |

Technical parameters :

| Serial No. | Parameter | Description |
| --- | --- | --- |
| 1 | Panel Material | Aluminum alloy |
| 2 | Surface finish | Electroplated/Painted/Power sprayed |
| 3 | Panel Dimension(mm) | 165*125; |
| 4 | Cutout(mm) | 148x115 |
| 5 | Height of product(mm) | 95 |
| 6 | Bottom box size(mm) | 146*113*95 |
| 7 | Bottom box material | Plastic |
| 8 | Capacity of modules /Interface size | 6 ways |
| 9 | Configuration | Power outlet+Data outlet or USB charging : Customized as required |
| 10 | Cable length | 1.5m, 2m,2m or required length |
| 11 | Available modules: | 45*45mm Type series |

Application:

Features:

1.Wireless charging function as per QI standard;

2. Wiredrawing oxidation fifinish with wireless charging socket;

3. Dual USB port, full-voltage USB smart quick charge, supporting QC3.0; Carrying QUALCOMM identifification chip, power conversion  rate of above 80%, and at the same time, a varity of intelligent protection functions including overcharge protection,over- temperature protection, overvoltage protection, short circuit  protection, under-voltage protection, overload protection, etc. overvoltage protection, short-circuit protection, under-voltage protection, overload protection, etc.

Product Show:

FZ-510 Outline drawing:

Available sockets or modules types:

Package:20 Pcs inner box into a master carton.Poly bag with box packing.