Wenzhou Safewire Electric CO.,Ltd.

SPECIFICATION  SHEET

PRODUCT NAME:     Open coverplate socket

PRODUCT No.:    HTD-210CK

Address:2nd floor, Wealth Garden, Liushi town, Yueqing,  Wenzhou,China ,325604

Tel:0086-577-61725369

Mob:0086-18612380398

ZIP:325604

（E-mail）：info@safewirele.com

(WEB):  http://www.safewirele.com

Quick Details:

| Serial No. | Parameter | Description |
| --- | --- | --- |
| 1 | Safewire item | HTD-210CK |
| 2 | Surface finish | Wire drawing/Polishing/Spray painting |
| 3 | Panel Dimension(mm) | 210*210 |
| 4 | Cutout(mm) | 198x198 |
| 5 | Capacity of modules | 10 ways modules |
| 6 | Mounting type | Declining installation |
| 7 | Sink box Material | Steel+Zinc plated |
| 8 | Base box dimension(mm) | 190*190*75 |
| 9 | Available modules | 45*45/45*22.5(mm) |

Application:

1.Feature of Safewire floorbox:

- Customzation design & production: ODM & OEM as per samples or drawing by each of us.

- Supply with SKD parts or finished products, save cost: save cost, save money for you!

- Flush-mounting & Recess-mounting in Access floor & Recess floor

- Advantage of Safewire floorbox :

- Patent Retractable cable entry design:

- More affordable MOQ less than 100 units:

- More internation socket , multimedia and Data accessories :

3.Specification of Safewire floorbox :

- .Product dimension:

- Available installation modules/socket/accessories:

Installation instructions:

- Cut out 198*198，Powering the slurry.

- Remove the pre-installed temporary lid,wiring and installing modules.

- Pre-installed cable pipe as per your request .

- Install cover lid and tighten with screws.

- Conceal the cut edge of carpet of flooring

Attentions:

1.When installing and wiring,Product should avoid direct contact with corrosive liquid, gas (strong acid, strong alkali, paint).

2.This product is suitable for dry surface treatment, avoid water flush and immersion, and ensure its insulation.This product is not suitable for use in wet areas.

3.All dimensions quotes are nominal only.Drawing images and specification are only for illustrative purposes and dimensions are subject to final confirmation by us.

Safety Warning：

1.This is a class I product and must be earthed

2.This product must be installed/wired by a qualified electrician

3.For indoor use only.

4.For concrete access floor.

# Text boxes

（3）

（1）

（2）

（5）

（4）