Wenzhou Safewire Electric CO.,Ltd.

SPECIFICATION  SHEET

PRODUCT NAME:  optical fiber

PRODUCT No.:    CD-14 series

ADD: 2nd floor, Wealth Garden, Liushi Town, Yueqing city,Wenzhou,Zhejiang,China

（TEL）:0086-577--61725369

（E-mail）：info@safewirele.com

(WEB):  http://www.safewirele.com

Characteristic

| Serial No. | Parameter | Description |
| --- | --- | --- |
| 1 | Product name | optical fiber |
| 2 | Model Number | CD-14 series |
| 3 | Place of Origin | Zhejiang,China |
| 4 | Brand Name | Safewire or OEM brand |
| 5 | Size | 23*36mm 128type socket |
| 6 | Color | White |
| 7 | Insertion Loss | ≤0.3dB |
| 8 | Return loss | ≥50dB |
| 9 | Durability (1000 Mating) | 0.2dB Max. |
| 10 | Operating Temperature | -40°C~+75°C |
| 11 | Storage Temperature | -40°C~+85°C |

Feature

1.Good performance and High success rate.

2.Easiness in installation with average splicing time of 15 sec

3.Special tool is simple and convenient to use.

4.Reusable and repeat orperation times are up to 100.

5.Integrated protection of the casing to prevent the connector form impact

6. On line tension is up to 20N to protect the connector from the draging

7. The maxmum tension is up to 100N. It’s the most safety connector

| The difference between each product model |
| --- |
| Item | Product description |
| CD-14-1A | LC optical fiber |
| CD-14-1B | SC optical fiber |
| CD-14-1C | FC optical fiber |

Product show

Application:
Use in floor box or desktop socket apllication in stage / Multimedia office ect.

RoHS Certificate of Compliance：Conforms with the Directive 2002/95/EC (ROHS) regarding to limitation of dangerous substances,in particular to clause 4 which forbids the use of  substances.

Package: 20 Pcs connector in poly bag separately with inner box. 10pcs inner boxes in one carton box.