Wenzhou Safewire Electric CO.,Ltd.

SPECIFICATION  SHEET

PRODUCT NAME:     Male XLR

PRODUCT No.:   CD-20-1 series

ADD: 2nd floor, Wealth Garden, Liushi Town, Yueqing city,Wenzhou,Zhejiang,China

（TEL）:0086-577--61725369

（E-mail）：info@safewirele.com

(WEB):  http://www.safewirele.com

Characteristic:

| Serial No. | Parameter | Description |
| --- | --- | --- |
| 1 | Product name | Male XLR |
| 2 | Place of Origin | Zhejiang,China |
| 3 | Brand Name | Safewire or OEM brand |
| 4 | Type | XLR |
| 5 | Pin number | 3pin female connector |
| 6 | Plastic materials | PBT PC |
| 7 | Metal material | Copper + Stainless steel |
| 8 | Contact Resistance | XLR:≤20MΩ JACK:≤30MΩ |
| 9 | Insulation Resistance | ≥500MΩ |
| 10 | Pressure | 500V,AC/Minute |
| 11 | Temperature Range | -30~+70℃ |
| 12 | Rated Voltage | 50V AC |
| 13 | Rated Current | 7.5A |
| 14 | Operating force | XLR:10N~50N JACK: 5N~30N |
| 15 | Lifetime | 5000 times |
| 16 | Size | 23*36mm |
| 17 | Application | Audio & Video |

Product show

Feature

| The difference between each product model |
| --- |
| Item | Product description |
| CD-20-1A | Male XLR/Canon solderless |
| CD-20-1B | Male XLR/Canon solder |

Application:

1.XLR socket is suitable for web live broadcast, radio station, karaoke and various balanced links.

2.Install Safewire floor box or desktop socket to use.

Package: 20 Pcs connector in poly bag separately with inner box. 10pcs inner boxes in one carton box.

Attentions:

1.Protect children from touch skirt of socket.

2.Ensure current and voltage as rating current/voltage .Do not overload

3.Prevent from corrosive liquid, gas (strong acid, strong alkali, paint)and humidity.

RoHS Certificate of Compliance：Conforms with the Directive 2002/95/EC (ROHS) regarding to limitation of dangerous substances,in particular to clause 4 which forbids the use of  substances: