Wenzhou Safewire Electric CO.,Ltd.

SPECIFICATION  SHEET

PRODUCT NAME: RJ11 Telephone

PRODUCT No.:          CD-4

ADD: 2nd floor, Wealth Garden, Liushi Town, Yueqing city,Wenzhou,Zhejiang,China

（TEL）:0086-577--61725369

（E-mail）：info@safewirele.com

(WEB):  http://www.safewirele.com

Characteristic

| Serial No. | Parameter | Description |
| --- | --- | --- |
| 1 | Product name | RJ11 Telephone |
| 2 | Model Number | CD-4 |
| 3 | Place of Origin | Zhejiang,China |
| 4 | Brand Name | Safewire or OEM brand |
| 5 | Size | 23*36mm |
| 6 | Color | White |
| 7 | Material | PC |
| 8 | Description | RJ11 Female Connector |
| 9 | Current rating | 1.5 AMP |
| 10 | Voltage Rating | 125 VAC RMS |
| 11 | Contact Resistance | 40 Milliohms max |
| 12 | Insulation Resistance | 1000 MEGOHMS MIN @ 500 VDC |
| 13 | Dielectric Strength | 1000 VAC RMS 60Hz, 1MIN |
| 14 | Storage | -40℃ TO +85℃ |

Product show

Application:
Use in floor box & desktop socket for home , hotel ,airport, office.

RoHS Certificate of Compliance：Conforms with the Directive 2002/95/EC (ROHS) regarding to limitation of dangerous substances,in particular to clause 4 which forbids the use of  substances.

Package: 20 Pcs connector in poly bag separately with inner box. 10pcs inner boxes in one carton box.