Wenzhou Safewire Electric CO.,Ltd.

SPECIFICATION  SHEET

PRODUCT NAME:  Desktop Socket

PRODUCT No. :    CK-06

ADD: 152 xinguang industrial zone, yueqing city, zhejiang province

（TEL）:0086-18612380398

（E-mail）：info@safewirele.com

(WEB):  http://www.safewirele.com

Product Details

| Serial No. | Parameter | Description |
| --- | --- | --- |
| 1 | Min Size | 2 modules |
| 2 | Max Size | 6.5 modules |
| 3 | Length(L) | No.of modules*53+85 mm |
| 4 | Dimension | L*102d*103h mm |
| 5 | Cut Hole | (L-30)*106d mm |
| 6 | Category | On desk,Under desk |
| 7 | Packaging | Regular white box packing |
| 8 | Certificate | UL,cUL,CCC,CE,RoHS |
| 9 | Anodized Aluminum Body | Clear,Black |
| 10 | Modules | White,Black |
| 11 | End Caps | Silver,Black |

Product Show:

Cancel the Figure:

Features:

- Easy to install without cutout on work surface3 mounting methods and 2 of them without tools required.

- Customized to any combination of power, data &custom modules.

- capable of daisy chain power connection.

- Customized module to combine power supply and weak current configuration on demand .

- Possess UL,cUL,CE,CCC, RoHS certificates.

Installation Instruction

Attentions:

Panel, Training Room, Work Station, Hotel Room

Attentions:

1.Don't touch the socket with wet hands when the power is on