Wenzhou Safewire Electric CO.,Ltd.

SPECIFICATION  SHEET

PRODUCT NAME: 5 pin socket

PRODUCT No.:         CP3-5

ADD: 2nd floor, Wealth Garden, Liushi Town, Yueqing city,Wenzhou,Zhejiang,China

（TEL）:0086-577--61725369

（E-mail）：info@safewirele.com

(WEB):  http://www.safewirele.com

Characteristic

| Serial No. | Parameter | Description |
| --- | --- | --- |
| 1 | Product name | Female XLR/Canon |
| 2 | Model Number | CP3-5 |
| 3 | Place of Origin | Zhejiang,China |
| 4 | Brand Name | Safewire or OEM brand |
| 5 | Size | 23*72mm 128type socket |
| 6 | Color | White |
| 7 | Connector | 5 pin |
| 8 | Contact Resistance | ≤30MΩ |
| 9 | Insulation Resistance | ≥2GΩ |
| 10 | Pressure | 2700V,AC/Minute |
| 11 | Temperature Range | -30~+70℃ |
| 12 | Rated Load | 250V AC 20A |
| 13 | Lifetime | 5000 times |

Feature

1.High Quality, Sturdy, Metal Construction. Easy to assemble.

2.Heavy-duty, molded connector design with internal strain relief to prolong its durability.

3.Locking Metal End, Perfect for making custom cables (DMX, MIC, microphone, audio ect.)

4.Single USB socket with five holes

Product show

Application:
  Use in floor box or desktop socket apllication in home / airport / hotel ect.

RoHS Certificate of Compliance：Conforms with the Directive 2002/95/EC (ROHS) regarding to limitation of dangerous substances,in particular to clause 4 which forbids the use of  substances.

Package: 20 Pcs connector in poly bag separately with inner box. 10pcs inner boxes in one carton box.