Wenzhou Safewire Electric CO.,Ltd.

SPECIFICATION  SHEET

PRODUCT NAME:      Desktop socket

PRODUCT No.:       FZ-526

Address:2nd floor, Wealth Garden, Liushi town, Yueqing,  Wenzhou,China ,325604

Tel:0086-577-61725369

Mob:0086-18612380398

ZIP:325604

（E-mail）：info@safewirele.com

(WEB):  http://www.safewirele.com

Technical parameters & characteristic :

- Working environment:

- The environment temperature:-5℃~/40℃

- The rated voltage：100V~~250V

- Rated current：10A、13A、16A、20A

- Characteristic:

| 1 | Model | HTD-526 | 6 | HS Code | 8536690000 |
| --- | --- | --- | --- | --- | --- |
| 2 | Brand Name | Safewire or OEM brand | 7 | Market standard | Customized |
| 3 | Type | floor socket | 8 | Place of origin | Zhejiang , Wenzhou, China |
| 4 | Color | silver | 9 | Frequency | 50Hz~60Hz |
| 5 | Grounding | Standard grounding | 10 | Current Type | AC |

- Technical parameters :

| Serial No. | Parameter | Description |
| --- | --- | --- |
| 1 | Material | Aluminum 6063, PC zinc alloy |
| 2 | Panel Material | Stainless/Brass |
| 3 | Surface finish | Painted/Oxygenated |
| 4 | Panel Dimension(mm) | φ124 |
| 5 | Cutout(mm) | φ100 |
| 6 | Dimension of product(mm) | 380 |
| 7 | Capacity of modules /Interface size | 8 ways 45*45mm modules |
| 8 | Configuration | Power outlet+Data outlet or USB charging : Customized as required |
| 9 | Cable length | 1.5m, 2m,3m or required length |
| 10 | Available modules | 45*45mm Type series |

Application：

- Office and education

- Industry and Engineering

- Presentation and retail;

- Orientation and safety;

- Transit areas and parking;

- Hotels, hospitality and wellness;

- Health, sport and leisure;

- Art and culture;

Product Show:

Features:

- Upside-down installation possible.Connection is simple and made on the pop up socket in upper position . The unit is then hidden under the desktop, enabling the modules to come out push& pull the opening.

- Enables the connection of 8 modules.

- Suitably installed into 120mm grommet hole.

- Casting made from aluminum and solid plastic.

- Suitable for desk tops up to 50mm;

- Coming with hardwired starter-or interlink cable. Also avaiable with 2.5mm internal wiring.

vailable for 45*45mm type international sockets or modules types:

FZ-526 Outline drawing:

Package:8 Pcs inner box into a master carton.Poly bag with box packing.

Installation Process

- Cut out φ100mm.

- Rotate the mounting ring thread first and remove it.

- Put the product into the opened hole.

- Rotate and tighten the mounting ring thread and secure the product to the table.

Attentions:

1.Prevent from corrosive liquid, gas (strong acid, strong alkali, paint)and humidity.

2. All dimension quoted are nominal only. Drawings , images and text are for illustrative perposes only and product details and dimension are subject to change without notice.

Safety Warning:

1)This is a class I product and must be earthed.

2)This product must be installed/wired by a qualified electrician.

3)before installation/maintnance ,ensure the mains supply is switched off and the circuit  fuses are removed or circuit breakers switch off.

4)For indoor use only.

# Text boxes

LVD test report

CE certificate by TUV,Germany

Mounting ring thread

Body and module