Wenzhou Safewire Electric CO.,Ltd.

SPECIFICATION  SHEET

PRODUCT NAME:     Pull Outlet Box

PRODUCT No.:       HTD-13

ADD: 2nd floor, Wealth Garden, Liushi Town, Yueqing city,Wenzhou,Zhejiang,China

（TEL）:0086-577-62799688

（E-mail）：info@safewirele.com

(WEB):  http://www.safewirele.com

Technical parameters & characteristic :

- Working environment:

- The environment temperature:-5℃~/40℃

- The rated voltage：100V~~250V

- Rated current：10A、13A、16A、20A

- Technical parameters :

| Serial No. | Parameter | Description |
| --- | --- | --- |
| 1 | Panel Material | Brass alloy/Stainless steel |
| 2 | Surface finish | Wire drawing/Polishing/Spray painting |
| 3 | Panel Dimension(mm) | 134*134 |
| 4 | Cutout(mm) | 122x122 |
| 5 | Static pressure | 1000N |
| 6 | Horizontal mounting | Horizontal installation |
| 7 | Sink box Material | Steel+Zinc plated |
| 8 | Hinged lid thickness | 4MM |
| 9 | Base box dimension(mm) | 122*122*71.5 |
| 10 | Available modules | 45*45/45*22.5(mm) modules |
| 11 | Colors | silver/Golden |
| 12 | Module Capacity | 6 |
| 13 | Material | Aluminum alloy/Brass alloy |

Features:

1.Economic range with large capacity.
2.The sleek & flat designed cover top with beveled edges allows the unit to mount flush with the surface.
3.Features double easy to use flip lids which provides quick access to power and data outlets.
4.Ideal for concrete floors and countertop applications.

Product Show:

HTD-13 Outline drawing:

Application:

Package:12 Pcs inner box into a master carton.Poly bag with box packing.

Installation instructions:

- Cut out 122*122(mm)，Powering the slurry.

- Remove the pre-installed temporary lid,wiring and installing modules,Per-installthe cable pipe                   as per your request .

- Install cover lid and tighten with screws.

- Conceal the cut edge of carpet of flooring

Attentions:

1.When installing and wiring,Product should avoid direct contact with corrosive liquid, gas (strong acid, strong alkali, paint).

2.This product is suitable for dry surface treatment, avoid water flush and immersion, and ensure its insulation.This product is not suitable for use in wet areas.

3.All dimensions quotes are nominal only.Drawing images and specification are only for illustrative purposes and dimensions are subject to final confirmation by us.

Safety Warning：

1.This is a class I product and must be earthed

2.This product must be installed/wired by a qualified electrician

3.For indoor use only.

# Text boxes

（1）

（2）

（4）

（3）